## Slide 1: Biomedical Control Systems (BCS)
Module Leader: Dr Muhammad Arif
Email: muhammadarif13@hotmail.com
Batch: 10 BM
Year: 3rd
Term: 2nd
Credit Hours (Theory): 4
Lecture Timings: Monday (12:00-2:00) and Wednesday (8:00-10:00)
Starting Date: 16 July 2012
  Office Hour: BM Instrumentation Lab on Tuesday and Thursday (12:00 – 2:00)
  Office Phone Ext: 7016
  Please include “BCS-10BM" in the subject line in all email communications to avoid auto-deleting or junk-filtering.

## Slide 2: The Bode Plot
A Frequency Response Analysis Technique

## Slide 3: The Bode Plot
The Bode plot is a most useful technique for hand plotting was developed by H.W. Bode at Bell Laboratories between 1932 and 1942.
This technique allows plotting that is quick and yet sufficiently accurate for control systems design.
The idea in Bode’s method is to plot magnitude curves using a logarithmic scale and phase curves using a linear scale.
The Bode plot consists of two graphs:
i. A logarithmic plot of the magnitude of a transfer function.
ii. A plot of the phase angle.
Both are plotted against the frequency on a logarithmic scale.
The standard representation of the logarithmic magnitude of G(jw) is 20log|G(jw)| where the base of the logarithm is 10, and the unit is in decibel (dB).

## Slide 4: Advantages of the Bode Plot
Bode plots of systems in series (or tandem) simply add, which is quite convenient.
The multiplication of magnitude can be treated as addition.
Bode plots can be determined experimentally.
The experimental determination of a transfer function can be made simple if frequency response data are represented in the form of bode plot.
The use of a log scale permits a much wider range of frequencies to be displayed on a single plot than is possible with linear scales.
Asymptotic approximation can be used a simple method to sketch the log-magnitude.

## Slide 5: Asymptotic Approximations: Bode Plots
The log-magnitude and phase frequency response curves as functions of log ω are called Bode plots or Bode diagrams.
Sketching Bode plots can be simplified because they can be approximated as a sequence of straight lines.
Straight-line approximations simplify the evaluation of the magnitude and phase frequency response.
We call the straight-line approximations as asymptotes.
The low-frequency approximation is called the low-frequency asymptote, and the high-frequency approximation is called the high-frequency asymptote.

## Slide 6: Asymptotic Approximations: Bode Plots
The frequency, a, is called the break frequency because it is the break between the low- and the high-frequency asymptotes.
Many times it is convenient to draw the line over a decade rather than an octave, where a decade is 10 times the initial frequency.
Over one decade, 20logω increases by 20 dB.
Thus, a slope of 6 dB/octave is equivalent to a slope of 20 dB/ decade.
Each doubling of frequency causes 20logω to increase by 6 dB, the line rises at an equivalent slope of 6 dB/octave, where an octave is a doubling of frequency.
In decibels the slopes are n × 20 db per decade or n × 6 db per octave (an octave is a change in frequency by a factor of 2).

## Slide 7: Classes of Factors of Transfer Functions
Basic factors of G(jw)H(jw) that frequently occur in an arbitrarily transfer function are
Class-I: Constant Gain factor, K
Class-II: Integral and derivative factors,
Class-III: First order factors,
Class-IV: Second order factors,

## Slide 8: Class-I: The Constant Gain Factor (K)
If the open loop gain K
Then its Magnitude (dB) = constant
And its Phase
The log-magnitude plot for a constant gain K is a horizontal straight line at the magnitude of 20logK decibels.
The effect of varying the gain K in the transfer function is that it raises or lowers the log-magnitude curve of the transfer function by the corresponding amount.
The constant gain K has no effect on the phase curve.

## Slide 9: Example1 of Class-I: The Factor Constant Gain K
K = 20
K = 10
K = 4
K = 4, 10, and 20

## Slide 10: Example2 of Class-I: when G(s)H(s) = 6 and -6
20log|G(jω)H(jω)|
ω
0
Magnitude (dB)
15.5
Frequency (rad/sec)
G(jω)H(jω)
ω
0o
Phase (degree)
Frequency (rad/sec)
20log|G(jω)H(jω)|
ω
0
Magnitude (dB)
15.5
Frequency (rad/sec)
G(jω)H(jω)
ω
0o
Phase (degree)
Frequency (rad/sec)
-180o
Bode Plot for G(jω)H(jω) = 6
Bode Plot for G(jω)H(jω) = -6

## Slide 11: Corner Frequency or Break Point
The low frequency asymptote () and high frequency asymptote () are intercept at 0 dB line when ωT=1 or , that is the frequency of interception and is called as corner frequency or break point or break frequency.

## Slide 12: Class-II: The Integral Factor
If the open loop gain ,
Magnitude (dB)
When the above equation is plotted against the frequency logarithmic, the magnitude plot produced is a straight line with a negative slope of 20 dB/ decade.
Phase
When the above equation is plotted against the frequency logarithmic, the phase plot produced is a straight line at -90°.
Corner frequency or break point ω = 1 at the magnitude of 0 dB.

## Slide 13: Example1 of Class-II: The Factor
The slope intersects with 0 dB line at frequency ω =1
A slope of 20 dB/dec
for magnitude plot of factor
A straight horizontal line at 90° for phase plot of factor

## Slide 14: Example2 of Class-II: The Factor
The frequency response of the function G(s) = 1/s, is shown in the Figure.
The Bode magnitude plot is a straight line with a -20 dB/decade slope passing through zero dB at ω = 1.
The Bode phase plot is equal to a constant -90o.

## Slide 15: Class-II: The Derivative Factor
If the open loop gain
Magnitude (dB)
When the above equation is plotted against the frequency logarithmic, the magnitude plot produced is a straight line with a positive slope of 20 dB/ decade.
Phase
When the above equation is plotted against the frequency logarithmic, the phase plot produced is a straight line at 90°.
Corner frequency or break point ω = 1 at the magnitude of 0 dB.

## Slide 16: Example of Class-II: The Factor Jω
The frequency response of the function G(s) = s, is shown in the Figure.
G(s) = s has only a high-frequency asymptote, where s = jω.
The Bode magnitude plot is a straight line with a +20 dB/decade slope passing through 0 dB at ω = 1.
The Bode phase plot is equal to a constant +90o.

## Slide 17: Class-II (Generalize form): The Factor
Generally, for a factor
Magnitude (dB)
Phase
Corner frequency or break point ω = 1 at the magnitude of 0 dB.
For Example the magnitude and phase plot for factor
Magnitude (dB) =
Phase 2(90o) = 180o
In decibels the slopes are ±P × 20 dB per decade or ±P × 6 dB per octave (an octave is a change in frequency by a factor of 2).

## Slide 18: Example1 of Class-II (Generalize): The Factor

## Slide 19: Example2 of Class-II (Generalize): The Factor

## Slide 20: Class-III: First Order Factors,
If the open loop gain , where T is a real constant.
Magnitude (dB)
When , then magnitude dB,
The magnitude plot is a horizontal straight line at 0 dB at low frequency (ωT << 1).
When , then magnitude
The magnitude plot is a straight line with a slope of -20 dB/decade at high frequency (ωT >> 1).
Low-Frequency Asymptote (letting frequency s 0)
High-Frequency Asymptote (letting frequency s ∞)

## Slide 21: Class-III: First Order Factors,
The low frequency asymptote () and high frequency asymptote () are intercept at 0 dB line when ωT=1 or , that is the frequency of interception and is called as corner frequency or break point or break frequency.
At corner frequency, the maximum error between the plot obtained through asymptotic approximation and the actual plot is 3 dB.
Phase
When , then phase
(So it’s a horizontal straight line at 0o until ω=0.1/T)
When , then phase
(it’s a horizontal straight line with a slope of -45o/decade until ω=10/T)
When , then phase
(So it’s a horizontal straight line at -90o)

## Slide 22: Example1 of Class-III: First Order Factors,
Bode Diagram for Factor (1+jω)-1

## Slide 23: Example2 of Class-III: The Factor
Problem: find the Bode plots for the transfer function G(s) = 1/(s + a), where s = jω, and a is the constant which representing the break point or corner frequency.
Low-Frequency Asymptote (letting frequency s 0)
When , then the magnitude =
The Bode plot is constant until the break frequency, a rad/s, is reached.
When , then the phase

## Slide 24: Example2 of Class-III: The Factor
Continue:
High-Frequency Asymptote (letting frequency s ∞)
When , then the magnitude
Magnitude (dB):
Phase(degree):
When , then the phase

## Slide 25: Example2 of Class-III: First Order Factors,
The normalized Bode of the function G(s) = 1/(s+a), is shown in the Figure.
where s = jω and a is break point or corner frequency.
The phase plot begins at 0o and reaches -90o at high frequencies, going through -45o at the break frequency.
The high-frequency approximation equals the low frequency approximation when ω = a, and decreases for ω > a.
The Bode log magnitude diagram will decrease at a rate of 20 dB/decade after the break frequency.

## Slide 26: Class-III: First Order Factors,
If the open loop gain , where T is the real constant.
Then its Magnitude (dB)
When , then magnitude dB,
The magnitude plot is a horizontal straight line at 0 dB at low frequency (ωT << 1).
When , then magnitude
The magnitude plot is a straight line with a slope of 20 dB/decade at high frequency (ωT >> 1).
Low-Frequency Asymptote (letting frequency s 0)
High-Frequency Asymptote (letting frequency s ∞)

## Slide 27: Class-III: First Order Factors,
The Phase will be
When , then phase
(So it’s a horizontal straight line at 0o until ω=0.1/T)
When , then phase
(it’s a horizontal straight line with a slope of 45o/decade until ω=10/T)
When , then phase
(So it’s a horizontal straight line at 90o)

## Slide 28: Example3 of Class-III: First Order Factors,

## Slide 29: Example4 of Class-III: First Order Factors,
The normalized Bode of the function G(s) = (s + a), is shown in the Figure.
where s = jω and a is break point or corner frequency.
The phase plot begins at 0o and reaches +90o at high frequencies, going through +45o at the break frequency.
The high-frequency approximation equals the low frequency approximation when ω = a, and increases for ω > a.
The Bode log magnitude diagram will increases at a rate of 20 dB/decade after the break frequency.

## Slide 30: Example-5: Obtain the Bode plot of the system given by the transfer function;
We convert the transfer function in the following format by substituting s = jω
We call ω = 1/2 , the break point or corner frequency. So for
So when ω << 1 , (i.e., for small values of ω), then G( jω ) ≈ 1
Therefore taking the log magnitude of the transfer function for very small values of ω, we get
Hence below the break point, the magnitude curve is approximately a constant.
So when ω >> 1, (i.e., for very large values of ω), then
(1)

## Slide 31: Example-5: Continue.
Similarly taking the log magnitude of the transfer function for very large values of ω, we have;
So we see that, above the break point the magnitude curve is linear in nature with a slope of –20 dB per decade.
The two asymptotes meet at the break point.
The asymptotic bode magnitude plot is shown below.

## Slide 32: Example-5: Continue.
The phase of the transfer function given by equation (1) is given by;
So for small values of ω, (i.e., ω ≈ 0), we get φ ≈ 0.
For very large values of ω, (i.e., ω →∞), the phase tends to –90o degrees.
To obtain the actual curve, the magnitude is calculated at the break points and joining them with a smooth curve. The Bode plot of the above transfer function is obtained using MATLAB by following the sequence of command given.
num = 1;
den = [2 1];
sys = tf(num,den);
grid;
bode(sys)

## Slide 33: Example-5: Continue.
The plot given below shows the actual curve.