## Slide 1: Biomedical Control Systems (BCS)
Module Leader: Dr Muhammad Arif
Email: muhammadarif13@hotmail.com
Batch: 10 BM
Year: 3rd
Term: 2nd
Credit Hours (Theory): 4
Lecture Timings: Monday (12:00-2:00) and Wednesday (8:00-10:00)
Starting Date: 16 July 2012
  Office Hour: BM Instrumentation Lab on Tuesday and Thursday (12:00 – 2:00)
  Office Phone Ext: 7016
  Please include “BCS-10BM" in the subject line in all email communications to avoid auto-deleting or junk-filtering.

## Slide 2: The Nyquist Criterion
A Frequency Response Analysis Technique

## Slide 3: Nyquist Plot or Polar Plot
Nyquist Plots were invented by Nyquist - who worked at Bell Laboratories, the premiere technical organization in the U.S. at the time.
Nyquist Plots are a way of showing frequency responses of linear systems.
There are several ways of displaying frequency response data, including Bode' plots and Nyquist plots.
Bode' plots use frequency as the horizontal axis and use two separate plots to display amplitude and phase of the frequency response.
Nyquist plots display both amplitude and phase angle on a single plot, using frequency as a parameter in the plot.
Nyquist plots have properties that allow you to see whether a system is stable or unstable.

## Slide 4: Nyquist Plot
A Nyquist plot is a polar plot of the frequency response function of a linear system.
That means a Nyquist plot is a plot of the transfer function, G(s) with s = jω. That means you want to plot G(j ω).
G(j ω) is a complex number for any angular frequency, ω, so the plot is a plot of complex numbers.
The complex number, G(j ω), depends upon frequency, so frequency will be a parameter if you plot the imaginary part of G(j ω) against the real part of G(j ω).

## Slide 5: Sketch the Polar plot of Frequency Response
To sketch the polar plot of G(jω) for the entire range of frequency ω, i.e., from 0 to infinity, there are four key points that usually need to be known:
The start of plot where ω = 0,
The end of plot where ω = ∞,
Where the plot crosses the real axis, i.e., Im(G(jω)) = 0, and
Where the plot crosses the imaginary axis, i.e., Re(G(jω)) = 0.

## Slide 6: Problem-1: Polar Plot of Integrator
Consider a first order system,
Representing G(s) in the frequency response form G( jω ) by replacing s = jω:
The magnitude of G( jω ), i.e., | G( jω) |, is obtained as;
The phase of G( jω ), denoted by, φ , is obtained as;
Bode Plot
Polar Plot
Magnitude
Phase

## Slide 7: Problem-2: Polar Plot of First Order System
Consider a first order system
where T is the time constant.
Representing G(s) in the frequency response form G( jω ) by replacing s = jω:
The magnitude of G( jω ), i.e., | G( jω) |, is obtained as;
The phase of G( jω ), denoted by, φ , is obtained as;

## Slide 8
The start of plot where ω = 0
The end of plot where ω = ∞
The mid part of plot where ω = 1/T

## Slide 9
Polar Plot
Bode Plot
Magnitude
Phase

## Slide 10: Problem-3: Polar Plot of Second Order System
Consider a second order system
where T is the time constant.
Representing G(s) in the frequency response form G( jω ) by replacing s = jω:
The magnitude of G( jω ), i.e., | G( jω) |, is obtained as;
The phase of G( jω ), denoted by, φ , is obtained as;

## Slide 11
Polar Plot
The start of plot where ω = 0
The end of plot where ω = ∞

## Slide 12: Problem-4: Sketch the Nyquist diagram for the system shown in the following figure, and then determine the system stability using the Nyquist criterion.
(a)

## Slide 13
Point 1: The start of plot where ω = 0
Now that we have expressions for the magnitude and phase of the frequency response, we can sketch the polar plot using the 4 key points.

## Slide 14
Point 3: Where the plot crosses the real axis, i.e., Im(G(jω)) = 0
Point 2: The end of plot where ω = ∞
Take the imaginary part of equation (a), and put equal to zero, to get the value of frequency ω at the interception of real axis.

## Slide 15
Point 4: Where the plot crosses the imaginary axis, Re(G(jω)) = 0
Take the real part of equation (a), and put equal to zero, to get the value of frequency ω at the interception of imaginary axis.

## Slide 16: Problem-5: Sketch the polar plot for the following transfer function.
Representing G(s) in the frequency response form G( jω ) by replacing s = jω, and then Multiply both numerator and denominator by the conjugate of denominator.
(a)

## Slide 17
Point 1: The start of plot where ω = 0
At frequency ω = 0, we only observe the most significant terms that take the effect.
Magnitude at ω = 0:
Phase at ω = 0:
Point 2: The end of plot where ω = ∞
At frequency ω = ∞, we shall look at the most significant term that takes effect when the frequency approaches infinity.
Magnitude at ω = ∞:
Phase at ω = ∞:

## Slide 18
Point 3: Where the plot crosses the real axis, i.e., Im(G(jω)) = 0
Therefore, the intersection point between the polar plot and the real axis, when is located at;
Take the imaginary part of equation (a), and put equal to zero, to get the value of frequency ω at the interception of real axis.

## Slide 19
Point 4: Where the plot crosses the imaginary axis, Re(G(jω)) = 0
Therefore, the intersection point between the polar plot and the imaginary axis is when is located at;
Polar Plot
 | ¦G(jω)¦ | ∠G(jω)
ω = 0 | ∞ | -90o
ω = ∞ | 0 | -270o
Cross Re: |  | 
Cross Img: | 0 | 
 | ¦G(jω)¦ | ∠G(jω)
ω = 0 | ∞ | -90o
ω = ∞ | 0 | -270o
 | 0 | 
Take the real part of equation (a), and put equal to zero, to get the value of frequency ω at the interception of imaginary axis.

## Slide 20: Problem-6: Sketch the polar plot for the following transfer function.
Representing G(s)H(s) in the frequency response form G( jω )H(jω) by replacing s = jω:
The magnitude of GH(jω) i.e., |GH(jω)|, is obtained as;
The phase of GH(jω) denoted by, , is obtained as;

## Slide 21
Point 1: The start of plot where ω = 0
Point 2: The end of plot where ω = ∞
Polar Plot
 | ¦GH(jω)¦ | ∠GH(jω)
ω = 0 | ∞ | 0o
ω = ∞ | 0 | -90o

## Slide 25: Four Important Points for Derivation the Nyquist Criterion
The relationship between the poles of 1 + G(s)H(s) and the poles of G(s)H(s);
The relationship between the zeros of 1 + G(s)H(s) and the poles of the closed-loop transfer function, T(s);
The concept of mapping points;
The concept of mapping contours.

## Slide 26
It is conclude that;
The poles of 1 + G(s)H(s) are the same as the poles of G(s)H(s), the open-loop system.
The zeros of 1 + G(s)H(s) are the same as the poles of T(s), the closed-loop system.

## Slide 27: The Concept of Mapping
If we take a complex number s = x+jy on the s-plane and substitute it into a function, F(s), another complex number results. This process is called mapping.
OR
The term mapping is defined as the substitution of a complex number into a function, F(s), to get another complex number.
For example, substituting s = 4 + j3 into the function F(s) = (s2 +2s + 1) yields 16+j30. We say that 4 + j3 maps into 16+j30 through the function s2 +2s + 1.

## Slide 28: The Concept of Mapping Contours
The collection of points, called a contour.

## Slide 29: Examples of Contour Mapping
If we assume a clockwise direction for mapping the points on contour A, the contour B maps a clockwise direction if F(s) has just zeros or has just poles that are not encircled by the contour.

## Slide 30: Examples of Contour Mapping
The contour B maps in a counter clockwise direction if F(s) has just poles that are encircled by the contour, Also, you should verify that, if the pole or zero of F(s) is enclosed by contour A, the mapping encircles the origin .

## Slide 31: Examples of Contour Mapping
In this last case, the pole and zero rotation cancel, and the mapping does not encircle the origin.

## Slide 32: THE NYQUIST STABILITY CRITERION
A linear closed-loop continuous control system is absolutely stable if the roots of the characteristic equation have negative real parts.
Equivalently, the poles of the closed-loop transfer function, or the zeros of the denominator, 1 + GH(s), of the closed-loop transfer function, must lie in the left-half plane.
The Nyquist Stability Criterion establishes the number of zeros of 1 + GH(s) in the right-half plane directly from the Nyquist Stability Plot of GH(s).

## Slide 33: Nyquist Stability Criterion
The closed-loop control system whose open-loop transfer function is GH is stable if and only if
Where,
N = total number of CW encirclements of the (-1,0) point (i.e., GH = - 1 ) in the GH-plane.
Po = number of poles of GH in the right-hand-plane RHP for continuous systems.
If N > 0, the number of zeros Zo of 1 + GH in the RHP for continuous systems, is determined by
If N ≤ 0 and Po = 0, then the system is absolutely stable if and only if N = 0; that is, if and only if the (-1,0) point does not lie in the shaded region.

## Slide 34: Problem-7: Sketch the polar plot for the following transfer function and check the stability of the system.
There is one pole at the origin.
Representing G(s)H(s) in the frequency response form G( jω )H(jω) by replacing s = jω:
The magnitude of GH(jω) i.e., |GH(jω)|, is obtained as;
The phase of GH(jω) denoted by, , is obtained as;

## Slide 35
Point 1: The start of plot where ω = 0
Point 2: The end of plot where ω = ∞
Polar Plot
 | ¦GH(jω)¦ | ∠GH(jω)
ω = 0 | ∞ | -90o
ω = ∞ | 0 | -180o

## Slide 36
Nyquist or Polar Plot
Nyquist Diagram

## Slide 37
The region to the right of the contour has been shaded.
Clearly, the (-1,0) point is not in the shaded region; therefore it is not enclosed by the contour and so N ≤ 0.
The poles of GH(s) are at s = 0 and s = -1, neither of which are in the right-hand-plane RHP; hence Po = 0. Thus N = -Po = 0, and the system is absolutely stable.

## Slide 38
Problem-8: The Nyquist Stability Plot for GH(s) = 1/s(s-1) is given in the figure below.
The region to the right of the contour has been shaded and the (-1,0) point is enclosed; then N > 0. (It is clear that N = 1).
The poles of GH are at s = 0 and s = +1, the latter pole being in the RHP. Hence Po = 1.
N ≠ Po indicates that the system is unstable.
Z = N + Po = 1 + 1 = 2, therefore the poles of the closed-loop transfer function, or the zeros of the characteristic equation 1+GH in the right-hand plane RHP.